## Slide 1: CLASSIFICATION OF SIGNALS

## Slide 2: Causal and Non-causal Signals

## Slide 3: Anti-causal Signals
(a) Causal signal
(b) Anti-causal signal

## Slide 4: Right-sided and Left sided Signals

## Slide 5: Bounded and Unbounded Signals

## Slide 6
Deterministic & Non Deterministic Signals
Deterministic signals
Behavior of these signals is predictable w.r.t time
There is no uncertainty with respect to its value at any time.
These signals can be expressed mathematically.
Example x(t) = sin(3t) is a deterministic signal.

## Slide 7: Non Deterministic or Random signals
Behavior of these signals is random i.e. not predictable w.r.t time.
There is an uncertainty with respect to its value at any time.
These signals can’t be expressed mathematically.
Example: Thermal Noise

## Slide 8: Size of a Signal

## Slide 9: Energy Signal and Power Signal contd…
The signal energy does not indicate the actual energy of the signal because the signal energy depends on the load resistor. Hence, energy is defined as the energy dissipated in a normalized load of a 1-ohm resistor.
If a voltage x(t) is applied across a resistor R, the current through the resistor R is .
The instantaneous power in the circuit is given by
; ;
The total energy dissipated is integral of the instantaneous power.
The energy dissipated is E =
Substituting R= 1;
For a complex signal
The units of signal energy depends on the unit of the signal.

## Slide 11: Energy Signal and Power Signal contd...
Energy Signal : ENERGY will be FINITE and average POWER will be ZERO.
Example: Finite duration signals.
Power Signal : ENERGY will be INFINITE and average POWER will be FINITE.
Example: Periodic signals.
(a) Energy signal
(b) Power signal

## Slide 12: Signal Energy and Power contd…
Energy Signal
A signal with finite energy and zero power is called Energy Signal i.e.for energy signal
0 < E < ∞ and P =0
Energy of a signal is defined as the area under the square of the magnitude of the signal.

## Slide 13: Energy Signal and Power Signal contd…
Power Signal
Some signals have infinite signal energy. In that case it is more convenient to deal with average signal power.
For power signals
0 < P < ∞ and E = ∞
Average power of the signal is given by

## Slide 14: Signal Energy and Power contd…
Power Signal

## Slide 15: Check whether energy signal or power Signal

## Slide 16: Check whether energy signal or power Signal

## Slide 17: Contd….

## Slide 18: DT Energy Signal and Power Signal
The signal energy of a for a discrete time signal x[n] is
A discrtet time signal with finite energy and zero power is called Energy Signal i.e.for energy signal
0 < E < ∞ and P =0

## Slide 19: DT Energy Signal and Power Signal
The average signal power of a discrete time power signal x[n] is
For a periodic signal x[n] the average signal power is

## Slide 20: DT Energy Signal and Power Signal
Compute the total energy and average power of the given discrete time signals.
(a) x[n] = ramp[n]
x[n] = 0 n < 0
= n n ≥0
(b) y[n] = A
Ans  Neither energy signal nor power signal.
Ans  Power signal

## Slide 21: Thank You!